USER MANUAL

- SECURITY TIPS

WARNING!!! To reduce the risk of fire, electric shock, or injury to operator and others, follow these important safety instructions:

- Do not open fixture. Warranty will be void if opened or disassembled by anyone other that authorized Acue Lighting Technicians.

- Only connect to rated voltage range: AC110V-120V/60Hz or AC200V-240V / 50HZ (to be selected).

- Do not operate near open flames or flammable materials

- Fixture must be used in ambient temperatures: -15 ℃ -40 ℃, the highest temperature of the surface of the fixture should not increase 60 ℃.

- Keep away from the liquids and humid environments.

- Before using the lights you must ensure safe placement and do not operate with charger connected.

- If hanging the fixture, make sure the clamp being used is secured to the structure and to the fixture securely.

- Fixture is not recommended to be operated consecutively for more than 10 hours at a time

- Fixture should be turned off and disconnected from charger if a fault of any kind is detected.

- Fixture and charger must be checked for physical damage before each use (water, dust, dent, crack, tear, or fraying in wire)

2  TECHNICAL SPECIFICATIONS

Power Supply: AC 100-240V/50-60Hz

Power consumption: 50W

Light source: 4pcs*12W LED RGBWA+UV 6in1 mixing color

Beam Angle: 15°

Dimmer: 0-100% dimmer

Strobe rate:0-24HZ

Working Environment: -20˚- 40˚

IP rate: IP20, indoor

DMX Channels: 3CH, 4CH, 6CH, 10CH

Control Modes: DMX, Master-slave, Sound,Auto, Remote, Wireless DMX

Battery type: Lithium Ion

Battery Charge Time: 4 hours (full power)

Battery Life: (all on) 5hours, (single Color) 12hours

Battery Power: 11.1V, 6600mAh

Product size: 140*140*145mm

Net weight: 1.85kg

3  DISPLAY FUNCTIONS

MENU    UP  DOWN  ENTER

Operation Menu

| 1 | Address | DOO1-512 |
| --- | --- | --- |
| 2 | CH_Mode | 3CH |
|  |  | 4CH |
|  |  | 6CH |
|  |  | 10CH |
| 3 | Slnd | SLAVE |
|  |  | MAST |
| 4 | Manual control | Red 0-255 |
|  |  | Green 0-255 |
|  |  | Bule 0-255 |
|  |  | White 0-255 |
|  |  | Amber 0-255 |
|  |  | UV 0-255 |
| 5 | Mode | Color 1-15 |
|  |  | Auto 1-99 |
|  |  | Fade 1-99 |
|  |  | Sound 1-99 |
| 7 | Strobe | Strobe 1-99 |
| 8 | Battery | 000~100Hs |
| 9 | W512 | Wireless Off/On |
| 10 | Ir | Remote Off/On |

4  DMX CHANNEL CHART

| 3CH | 1CH | RED 0-255 |
| --- | --- | --- |
|  | 2CH | GREEN 0-255 |
|  | 3CH | BLUE 0-255 |
| 4CH | 1CH | RED 0-255 |
|  | 2CH | GREEN 0-255 |
|  | 3CH | BLUE 0-255 |
|  | 4CH | White 0-255 |
| 6CH | 1CH | RED 0-255 |
|  | 2CH | GREEN 0-255 |
|  | 3CH | BLUE 0-255 |
|  | 4CH | White 0-255 |
|  | 5CH | Amber 0-255 |
|  | 6CH | UV 0-255 |

| 10CH | 1CH | Master Dimmer |
| --- | --- | --- |
|  | 2CH | Strobe 0-255 |
|  | 3CH | RED 0-255 |
|  | 4CH | GREEN 0-255 |
|  | 5CH | BLUE 0-255 |
|  | 6CH | White 0-255 |
|  | 7CH | Amber 0-255 |
|  | 8CH | UV 0-255 |
|  | 9CH | Auto |
|  | 10CH | Speed |

5  FIXTURE MOUNTING

Please attach clamp firmly to fixture before hanging. The clamp can be fastened using the threaded hole for the bracket, then secure with a safety cable. The loading capacity of the safety cable should be 10 times that of the weight of the fixture itself.

6  DMX-512 CONNECTION

Please connect XLR-XLR control wire with every light from the output of DMX controller.

XLR connection:

ATTENTION: Please remember to connect a DMX signal terminator to the last fixture’s DMX output socket. Make sure the DMX signal terminator has a 120ohm resistor between terminals 2 and 3 of the XLR connector, connecting this signal terminator can avoid bad DMX signal transmission.

7  Troubleshooting

| Problems | Check list | Troubleshooting |
| --- | --- | --- |
| The fixture does not work | 1. Check if input voltage is correct 2. If the fuse has not popped 3. If the fixture is charged | 1. Make sure the voltage is correct. 2. Replace the same fuse. 3. Charge the fixture. |
| LED Dimmed Output | Check DMX dimmer level or dimmer level on control board | Adjust dimmer channel |
| No DMX input | 1. Check if polarity is reversed in the DMX controller. 2. If it is in DMX mode. 3. If there are 2 Master in a loop. | 1. Correct the DMX polarity. 2. Change to the DMX mode. 3. Set one piece into Slave mode. |
| Par Light setting works abnormality | 1. Check if the DMX address is correct. | 1. Set correct DMX address through display menu |

8  Maintenance

- Acue Lighting offers direct technical support to customers.

- If the machine has a problem and requires repair, please contact us and provide feedback as to what the problem is.

- Make sure power input cable is not damaged prior to connecting to charging port.

(

Warranty Card

Name     Model       Production  Purchase

End User: Company Name: Add:

Purchase Location Salesperson: Tel: Serial #

Please fill out and return warranty card with clear writing or else the warranty card will not be valid (warranty period and terms, see the following)

Warranty period：One year starting from purchase date

1. If product fails during regular use, you can contact us during the warranty period for warranty work and provide the warranty card and purchase.

2. The following will be the implementation of paid services:

(1)No effective warranty card

(2)There’s blank, alter and no point-of-sale name

(3)Damage caused by misuse

(4)Damage caused by transportation or unloading

(5)Damage caused by disassembly without authorization

(6)Damage caused by using an unauthorized control system

# Note:

Contents of this manual and product design are subject to change without notice. Acue Lighting retains the right to change specifications and design of product at its own discretion without prior notice. Thank you for your understanding.

For more information please contact Acue Lighting Inc by email at Info@AcueLighting.com or call our service center at (818) 646-7526.