Power Battery Bank

User Manual

This manual contains important information. Please read before operating fixture.

- SECURITY TIPS

WARNING!!! To reduce the risk of fire, electric shock, or injury to persons, follow these important safety instructions:

- Unit should not be opened by anyone other than a certified technician.

- Rated input voltage range: AC110V-120V/60Hz or AC200V

- -240V / 50HZ (to be selected).

- Do not expose unit to flammable materials. All flammable materials should maintain a distance of at least 3 feet from this fixture.

- Proper fixture operating ambient temperature: -15 ℃ -40 ℃, the highest temperature of operation should not exceed 60 ℃.

- Fixture should not be used in a humid environment.

- A proper clamp must be used when hanging the fixture using the supplied mounting bracket along with a safety cable.

- Fixture must be regularly inspected for damages prior to each use and before plugging in any other equipment to the power output source.

- Make sure all cooling ports are free of dust or any other blockage before every use. Blocked vent ports will result in permanent damage to fixture as well as the operator, or any products attached or near the fixture.

2  Technical Specifications

Input voltage: AC110-250V 50-60Hz

Output voltage:AC110V   50-60Hz

Battery Power:12V 40Ah

Battery Charge Time: 8hours

Battery type: Lithium Ion

Net Weight: 6.4kg

Product size: 338mm*268mm*126mm

Gross Weight: 7.5kg

Packaging size: 360mm*310mm*180mm(1pc/CTN)

3  Warranty and Service

- Acue Lighting offers technical support for the life of the product.

- Manufacturers Warranty is Valid for 1 Year after the date of purchase.

- If the machine is damaged and needs repairs, please contact your nearest service provider to start the repair process.

(

Warranty Card

Name     Model       Production  Purchase

End User Company Name: Add:

Sale Store: Location: Tel:

Proof of purchase is required for warranty to be valid (warranty period and terms, see the following)

Warranty period：one year from date of purchase

Manufacturers warranty only covers malfunctions caused by manufacturing defect. Warranty does not cover regular wear and tear or misuse of product by the end user.

The following will be the implementation of paid service:

(1) Non-effective warranty card

(2) If machine has been opened by anyone other than an Acue Lighting Service provider

(3) Failure caused by carelessness

(4) Failure caused by transportation or unloading

(5) Failure caused by operation outside the proper conditions (heat, cold, humidity, & etc)

(6) Failure caused by disassembly or alteration of products by unauthorized persons.

(7) Failure caused by using the improper power input/output

Acue Lighting Inc. reserves the rights to alter this product and all contents in this manual are subject to change without prior notification.