Technical Specifications:

Input Voltage: AC90-240V 50/60HZ

Power supply: 200W

Light Source: 1PCS*200W WW LED 3200K

DMX Channel Modes: 2CH/1CH

Operation: DMX512, Auto, Sound, Master-slave

User Manual

INTRODUCTION

Thank you so much to choose this product; it is adopting the most advanced lamps, which is called LED lamps. It conquers a lot of disadvantages such as power wasting, short using life, high temperature, etc. It has advantages of power saving, long life (it can reach 60,000.00 hours in general circs), high brightness, fresh colors…It is the best stage illuminating and various effect decorative products.

WARNINGS:

| No. | Show | Function | Instruction |
| --- | --- | --- | --- |
| 1 | d001 | DMX Address (001~512) | DMX-512 address set, 1 Channels mode |
| 2 | A001 | DMX Address (001~512) | DMX-512 address set, 2 Channels mode |
| 3 | C255 | Warm White (000~255) | UP、DOWN Change brightness |
| 4 | FH99 | Strobe flash (01~99) | UP、DOWN Change the speed |

1. Inspect the device carefully before installation in case of loose during transportation.

2. Don’t put the product on the shakable or moist place.

3 . Please keep the voltage stable, otherwise it will destroy the parts easily.

4. Check the voltage before turning on lamp. While power off, it needs 15minutes to cool before reconnecting the power.

5. Please keep the lamp dry and cool, .avoid working at 40℃ or above to guarantee its lifespan.

6 .Disconnect the power before installation or removing and ask professional technician to repair in case of malfunction. (Check fuses tube first).

| Channel | Function | Instruction |
| --- | --- | --- |
| CH1 | WARM WHITE Dimmer | Dimmer- Dark to Bright |
| CH2 | Strobe | White and Warm white strobe: from slow to fast |

Display function

DMX512Control： 1Channel Model(D001)

| Channel | Function | Instruction |
| --- | --- | --- |
| CH1 | WARM WHITE Dimmer | Dimmer- Dark to Bright |

DMX512Control：2Channel Model(A001)

For more information about this product as well as other products please visit www.AcueExpress.com

Or contact us directly:

Email: Info@AcueLighting.com

Phone: (818) 646-7526/ (818) 672-6822