USER MANUAL

1. INTRODUCTION

Thank you for choosing the Acue Lighting Design Brick RGBWW. In order to use this product correctly and safely, please read the instructions carefully before installing and using this product. This manual contains important installation and application information. Make sure to strictly follow the instructions when installing and operating this product. Retain this manual in a safe place for future reference

The Design Brick RGBWW uses a hard plastic and metal body, which is designed to withstand high temperatures. This product is designed and produced in strict accordance with CE standards, and conforms to the international standard of DMX512 signal protocol. It can be controlled manually from the display or through DMX using the built in 3 pin XLR in/out connectors. This fixture has multiple DMX channel modes to choose from. It is suitable for various types of concerts, theaters, studios, nightclubs, bars and other like environments.

2. Getting Started

Carefully remove the fixture from its packaging. Check whether the product has been damaged during transportation, and check whether the following contents are complete.

1x Design Brick RGBWW Fixture

1x Power cord

1x User manual

All fixtures have been tested thoroughly before leaving the factory. In order to keep the product in good condition and ensure safe operation, users should follow the safety precautions and warnings in this manual.

Important: Damages caused by not following the guidance in this user manual are not covered under warranty. The manufacturer is not responsible for product issues caused by misuse.

If the product has been exposed to extreme temperature environments during transportation or storage, please do not connect the product to the power mains immediately. High Heat as well as condensation or moisture due to temperature changes may damage the product. Only use it after the product has returned to normal temperature and after the product has been inspected for moisture. Maximum ambient operating temperature is 40˚C. Do not operate it where the temperature is higher than this.

This product can be used in the voltage range of 90-240V and is an indoor product. Please make sure that the power mains voltage used is not higher than what the product can withstand! ! The power plug must be inserted into a protected Class I socket and must be grounded properly.

3. Safety Information

●Please keep this User manual for future reference. All users of this product must read the user manual thoroughly.

●Make sure the fixture is properly grounded in order to avoid electric shock.

●The unit is for indoor use only. Use only in a dry location

●The unit must be installed in a location with adequate ventilation, at least 50cm from adjacent surfaces. Be sure that no ventilation slots are blocked

●Disconnect main power before replacement or servicing.

●Make sure there are no flammable materials close to the unit while operating as it is fire hazard.

●Use safety cable when mounting this unit.

●Maximum ambient operating temperature is 40℃. Do not operate it where the temperature is higher than this.

●Unit surface temperature may reach up to 85˚C. Do not touch the housing bare-handed during operation. Turn off the power and allow about 15 minutes for the unit to cool down before replacing or servicing

4: Connection of DMX512

The fixture uses the DMX512 signal control protocol with the ability to link multiple fixtures together using the built in 3-pin XLR connections located in the back of the fixture. When connecting the signal to multiple fixtures, it is best to use a double-core shielded DMX cable. Each fixture is connected through the internal DMX signal jacks (XLR Sockets) INPUT (input) and OUTPUT (output), and the 3-pin XLR plugs of fixture must correspond the order of fixtures. It is recommended to use a DMX signal terminator for the last fixture in the chain.

5: Display Instructions & DMX Addressing

MENU: function key  UP: plus key  DOWN: minus key  ENTER: confirm key

| Serial number | content | Numerical range | Function and description |
| --- | --- | --- | --- |
| 1 | d001 | 001- 512 | DMX512 address code setting-4 channel mode |
| 2 | A001 | 001- 512 | DMX512 address code setting-8 channel mode |
| 3 | r255 | 000 - 255 | Red dimming, from dark to bright. |
| 4 | G255 | 000 - 255 | Green dimming, from dark to bright. |
| 5 | b255 | 000 - 255 | Blue dimming, from dark to bright. |
| 6 | u255 | 000 - 255 | Warm White dimming, from dark to bright. |
| 7 | F255 | 000 - 255 | Above 5, the stroboscopic starts, the speed is from slow to fast, select the color through RGBU. |
| 8 | CL01 | 01-08 | Color output. |
| 9 | CC15 | 00 - 15 | Colorful jumps, from slow to fast. |
| 10 | DE15 | 00 - 15 | Colorful gradient, from slow to fast. |
| 11 | CP15 | 00 - 15 | The colorful pulse changes from slow to fast. |
| 12 | Soud | / | 7-color voice control color change |

Table (1) Comparison table of display window functions of digital tube

6: DMX Channel Table 4CH + 8CH

4-channel mode (d001 mode)

| aisle | Function | illustrate |
| --- | --- | --- |
| CH1 | R dimming | R dimming, from dark to bright |
| CH2 | G dimming | G dimming, from dark to bright |
| CH3 | B dimming | B dimming, from dark to bright |
| CH4 | WW dimming | WW dimming, from dark to bright |

- channel mode (A001 mode)

| Channel | Function | illustrate |
| --- | --- | --- |
| CH1 | Total dimming | R、G、B、WW total dimming, from dark to bright |
| CH2 | R dimming | R dimming, from dark to bright |
| CH3 | G dimming | G dimming, from dark to bright |
| CH4 | B dimming | B dimming, from dark to bright |
| CH5 | WW dimming | WW dimming, from dark to bright |
| CH6 | Total strobe | R, G, B, WW total strobe, from slow to fast |
| CH7 | Function selection | 0-50: CH1-CH6 control; 51-100: common color output (8 kinds); 101-150: jump change; 151-200: gradual change; 201-250 pulse change; 251-255: voice control |
| CH8 | Function speed | Function speed, from slow to fast (color selection during color output) |

7: Technical Specifications

Input Power: AC90~240V 50/60 Hz wide voltage range input

Max Power Draw: 240w

Light Source: 54pcs x 10w RGBWW LEDs

DMX Channel Modes: 8/4 DMX512 control channels can be set

Control Mode：Voice control\master-slave\self-propelled color change\DMX512

For more information about this product as well as other products please visit www.AcueExpress.com

Or contact us directly:

Email: Info@AcueLighting.com

Phone: (818) 646-7526/ (818) 672-6822