User Manual

Notice: Due to the constant work to improve product quality, we reserve the right to change all information in this manual without prior written notice. Publisher of this manual or manufacturer will not be responsible for information and/or corresponding results caused by this information.

- The Introduction of OLED panel

Operation instructions: press “MENU” to choose different options, press  or  to set the functions , press “ENTER” to confirm and save.

- OLED MENU

| TAB | LEVEL1 | LEVEL2 | LEVEL3 | LEVEL4 |
| --- | --- | --- | --- | --- |
| Addr(Address) | 001-512 | 001 |  |  |
| Chmd(Channel mode) | 29CH/11CH/119CH/108CH | 11CH |  |  |
| Stat(Static control) | R | 0-255 | 000 |  |
|  | G | 0-255 | 000 |  |
|  | B | 0-255 | 000 |  |
|  | W | 0-255 | 000 |  |
|  | Y | 0-255 | 000 |  |
|  | P | 0-255 | 000 |  |
| Set(Set) | CAL(Calibration) | R | 20--255 | 255 |
|  |  | G | 20--255 | 255 |
|  |  | B | 20--255 | 255 |
|  |  | W | 20--255 | 255 |
|  |  | Y | 20--255 | 255 |
|  |  | P(UV) | 20--255 | 255 |
|  | Reverse | YES/NO |  |  |
|  | DMX HOLD | ON/OFF DMX |  | OFF |
|  | LOCK(Key 2 minutes lock) | YES/NO | no |  |
| Auto(Auto) | Mode | Sound 1 |  | AUTO 3 |
|  |  | Sound 2 |  |  |
|  |  | Auto0 3 |  |  |
|  |  | ...... |  |  |
|  |  | Auto 11 |  |  |
|  | Speed | 0--100 |  | 50 |
| Info（Information ) | SOFT(Software version) |  |  |  |
|  | TEMP |  |  |  |
| Load(Load) | SET L（Setting load) | YES/NO |  |  |
| Send(Send) | YES/NO | COPY the Default setting to slave lights |  | NO |

- DMX Chart 11CH Mode

| Channels | Function | Description |
| --- | --- | --- |
| CH1 | Dimmer | RGBWYUV master dimmer, 0~100% linear dimming,dark ->bright |
| CH2 | Strobe | RGBWYUV master strobe, slow->fast |
| CH3 | Macro1 | 0--14： Empty 15--34： Color flow(Jump)（CH1--5 enable） 35--54： Color flow(Fade)（CH1--5 enable） 55--74： Color choose（CH1 enable） 75--94： Color Jump（CH1 enable） 95--114： Color fade,Color pulse（CH1 enable） 115--134：Effects 1（CH1 enable） 135--154：Effects2（CH1 enable） 155--174：Effects3（CH1 enable） 175--194：Effects4（CH1 enable） 195--214：Effects5（CH1 enable） 215--234：Effects6（CH1 enable） 235--255：Sound active（CH1 enable） |
| CH4 | Macro2 | 0--15： Empty 16--45： Effects1（CH1 ,CH6~CH11 enable） 56--60： Effects2（CH1 ,CH6~CH11 enable） 96--45： Effects3（CH1 ,CH6~CH11 enable） 136--60： Effects4（CH1 ,CH6~CH11 enable） 176--45： Effects5（CH1 ,CH6~CH11 enable） 240--255：Effects6（CH1 ,CH6~CH11 enable） |
|  | Macro3 | The direction of Color flow 0--127: flow left 128--255: flow right |
| CH5 | Macro speed 1 | Macro speed, slow->fast |
| CH6 | R dimmer | R dimming, 0~100% linear dimming, dark ->bright |
| CH7 | G dimmer | G dimming, 0~100% linear dimming, dark ->bright |
| CH8 | B dimmer | B dimming, 0~100% linear dimming, dark ->bright |
| CH9 | W dimmer | W dimming, 0~100% linear dimming, dark ->bright |
| CH10 | Y dimmer | Y dimming, 0~100% linear dimming, dark ->bright |
| CH11 | UV dimmer | UV dimming, 0~100% linear dimming, dark ->bright |

- DMX Chart 29CH Mode

| Channels | Function | Description |
| --- | --- | --- |
| CH1 | Dimmer | RGBWYUV master dimmer, 0~100% linear dimming, dark ->bright |
| CH2 | Strobe | RGBWYUV master strobe, slow->fast |
| CH3 | Macro1 | 0--14： Empty 15--34： Color flow(Jump)（CH1--5 enable） 35--54： Color flow(Fade)（CH1--5 enable） 55--74： Color choose（CH1 enable） 75--94： Color Jump（CH1 enable） 95--114： Color fade,Color pulse（CH1 enable） 115--134：Effects 1（CH1 enable） 135--154：Effects2（CH1 enable） 155--174：Effects3（CH1 enable） 175--194：Effects4（CH1 enable） 195--214：Effects5（CH1 enable） 215--234：Effects6（CH1 enable） 235--255：Sound active（CH1 enable） |
| CH4 | Macro2 | 0--15： Empty 16--45： Effects1（CH1 ,CH6~CH11 enable） 56--60： Effects2（CH1 ,CH6~CH11 enable） 96--45： Effects3（CH1 ,CH6~CH11 enable） 136--60： Effects4（CH1 ,CH6~CH11 enable） 176--45： Effects5（CH1 ,CH6~CH11 enable） 240--255：Effects6（CH1 ,CH6~CH11 enable） |
|  | Macro3 | The direction of Color flow 0--127: flow left 128--255: flow right |
| CH5 | Macro speed 1 | Macro speed, slow->fast |
| CH6 | R dimmer | R dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH7 | G dimmer | G dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH8 | B dimmer | B dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH9 | W dimmer | W dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH10 | Y dimmer | Y dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH11 | UV dimmer | UV dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH12 | LED1 dimmer | RGBWYUV dimming |
| CH13 | LED2 dimmer | RGBWYUV dimming |
| CH14 | LED3 dimmer | RGBWYUV dimming |
| CH15 | LED4 dimmer | RGBWYUV dimming |
| ...... | ....... | .......... |
| CH29 | LED18 dimmer | RGBWYUV dimming |

- DMX Chart 108CH Mode

| Channels | Function | Description |
| --- | --- | --- |
| CH1 | R1 dimmer | R1 dimming, 0~100% linear dimming, dark ->bright |
| CH2 | G1 dimmer | G1 dimming, 0~100% linear dimming, dark ->bright |
| CH3 | B1 dimmer | B1 dimming, 0~100% linear dimming, dark ->bright |
| CH4 | W1 dimmer | W1 dimming, 0~100% linear dimming, dark ->bright |
| CH5 | Y1 dimmer | Y1 dimming, 0~100% linear dimming, dark ->bright |
| CH6 | UV1 dimmer | UV1 dimming, 0~100% linear dimming, dark ->bright |
| CH7 | R2 dimmer | R2 dimming, 0~100% linear dimming, dark ->bright |
| CH8 | G2 dimmer | G2 dimming, 0~100% linear dimming, dark ->bright |
| CH9 | B2 dimmer | B2 dimming, 0~100% linear dimming, dark ->bright |
| .......... | .......... | .......... |
| CH108 | UV18 dimmer | UV18 dimming, 0~100% linear dimming, dark ->bright |

- DMX Chart 119CH Mode

| Channels | Function | Description |
| --- | --- | --- |
| CH1 | Dimmer | RGBWYUV master dimmer, 0~100% linear dimming, dark ->bright |
| CH2 | Strobe | RGBWYUV master strobe, slow->fast |
| CH3 | Macro1 | 0--14： Empty 15--34： Color flow(Jump)（CH1--5 enable） 35--54： Color flow(Fade)（CH1--5 enable） 55--74： Color choose（CH1 enable） 75--94： Color Jump（CH1 enable） 95--114： Color fade,Color pulse（CH1 enable） 115--134：Effects 1（CH1 enable） 135--154：Effects2（CH1 enable） 155--174：Effects3（CH1 enable） 175--194：Effects4（CH1 enable） 195--214：Effects5（CH1 enable） 215--234：Effects6（CH1 enable） 235--255：Sound active（CH1 enable） |
| CH4 | Macro2 | 0--15： Empty 16--45： Effects1（CH1 ,CH6~CH11 enable） 56--60： Effects2（CH1 ,CH6~CH11 enable） 96--45： Effects3（CH1 ,CH6~CH11 enable） 136--60： Effects4（CH1 ,CH6~CH11 enable） 176--45： Effects5（CH1 ,CH6~CH11 enable） 240--255：Effects6（CH1 ,CH6~CH11 enable） |
|  | Macro3 | The direction of Color flow 0--127: flow left 128--255: flow right |
| CH5 | Macro speed 1 | Macro speed, slow->fast |
| CH6 | R dimmer | R dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH7 | G dimmer | G dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH8 | B dimmer | B dimming, 0~100% linear dimming, dark ->bright(priority)） |
| CH9 | W dimmer | W dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH10 | Y dimmer | Y dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH11 | UV dimmer | UV dimming, 0~100% linear dimming, dark ->bright(priority) |
| CH1 | R1 dimmer | R1 dimming, 0~100% linear dimming, dark ->bright |
| CH2 | G1 dimmer | G1 dimming, 0~100% linear dimming, dark ->bright |
| CH3 | B1 dimmer | B1 dimming, 0~100% linear dimming, dark ->bright |
| CH4 | W1 dimmer | W1 dimming, 0~100% linear dimming, dark ->bright |
| CH5 | Y1 dimmer | Y1 dimming, 0~100% linear dimming, dark ->bright |
| CH6 | UV1 dimmer | UV1 dimming, 0~100% linear dimming, dark ->bright |
| CH7 | R2 dimmer | R2 dimming, 0~100% linear dimming, dark ->bright |
| CH8 | G2 dimmer | G2 dimming, 0~100% linear dimming, dark ->bright |
| CH9 | B2 dimmer | B2 dimming, 0~100% linear dimming, dark ->bright |
| .......... | .......... | .......... |
| CH119 | UV18 dimmer | UV18 dimming, 0~100% linear dimming, dark ->bright |

- Fixture features

Easy to operate, versatile design, flicker free, & quiet. Fixture is suitable for on-camera use in tv studios, concerts, corporate events, and permanent installations.

- Dimensions

- Technical Specifications

- Voltage: AC100~240V, 50/60HZ

- Light source: 18PCS 30W RGBWAUV 6in1 LED’s

- DMX Channel: 11/29/108/119CH

- Dimmer: High resolution dimmer 0~100%

- Lenses: 45mm 10/12/25/40degree optional

- Operate: Setup and addressing via OLED display and 4 buttons

- Pixel Pitch: 52MM

- Filter: Quick release diffusion filter

- RDM: support

- Working temperature: -30°C~50°C

- Control mode: DMX512, Auto Run, Master/Slave, Sound active

- RGBWAUV 16-bit color mixing

- Pattern effects with variable speed and fade time

- Strobe effect: Variable speed (1-20HZ)

- Horizontal hanging with Omega brackets

- Horizontal installation on the floor with tilt bracket fast locks

- Vertical installation on the floor with a base plate

- Hanging vertically “dropped” with a vertical adapter

- Split Joint: structural connection with 2 pieces quick release pins

- Housing: Aluminum, Black

- Data: 3 pin & 5 pin XLR IN/OUT Power con IN / OUT

- IP Grade: IP20

- Weight: 9.0 kg

For more information about this product or other Acue Lighting products, please visit www.AcueExpress.com or email us at Info@acuelighting.com.

©Acue Lighting, inc. 2022